## Slide 1: Wireless Networking from Technology For All to sub-THz
Edward Knightly http://networks.rice.edu

## Slide 2: Technology For All Wireless Project
2003 NSF ITR grant on “Transit Access Points”
Houston Chronicle front page story
Challenge from Technology For All founder
  Mission: “Empower under-resourced communities through technology”
  Missing link: broadband access

## Slide 3: Lab to Urban Field Trial
Expanded goal: urban-scale deployment
Custom s/w and h/w TAPs
  Access tier for all neighbors in the block
  Multi hop backhaul to inter-connect
  Capacity injection to scale capacity

## Slide 4: Result: First Multi-tier Urban Mesh Network
ISP for over 1,000 users/km2 in Houston’s under-served under- resourced neighborhoods
At scale experimental research in wireless networks
  Asymmetric topology and starvation
  Network architecture
  Multi-hop congestion mechanisms
  Network measurement and modeling

## Slide 5: Outlawed?

## Slide 6: Impacts
Disruptive industry shift
  Wi-Fi as a public Internet entry point
  Mesh networking industry: $5B today
Standards
  IEEE 802.11s (mandatory since Wi-Fi 5)
Societal: Broadband for underserved communities
  Transformative impact for education and job search
  Previously, “digital citizen” limited to higher incomes

## Slide 7: Houston Super Wi-Fi Trial
Community challenge: reliability (coverage gaps)
NSF NetSE large and MRI
First residential Super Wi-Fi
  Unused UHF TV channel
  Tower to home
– Research in spectrum sharing and
diverse spectrum access
TAPs FPGA
and custom UHF front end

## Slide 8: The Press…

## Slide 9: Next Day…
Incumbents (TV broadcasters) did not want to share spectrum
Critical for operational network to demonstrate value of shared spectrum and unlicensed spectrum

## Slide 10: Today…
FCC continues to open spectrum for unlicensed and shared access
Spectrum sharing capabilities in Wi-Fi APs
– Wi-Fi in 6 GHz bands
5G deployments in CBRS and diverse spectrum
Spectrum from 100 MHz to 6 GHz
Massive MIMO

## Slide 11: Looking Forward: The Next Wireless Network
New capabilities and performance milestones
  Tb/sec, mobile, low latency, robust, and secure
Millimeter wave to sub-THz spectrum
  GHz vs. MHz scale bandwidth
  High resolution sensing fused with communications
  High directivity for spatial multiplexing
Newly enabled applications
  High resolution sensing with UAV networks
  Wireless virtual and augmented reality: 10’s of Gb/sec/m2

## Slide 12: State of the Art: Wi-Fi at 60 GHz

## Slide 13: Wi-Fi at 60 GHz
Antenna array with analog/RF beam steering
Predefined codebook weights create virtual “sectors”
Up to 128 sectors per device (3° beam width)
Mechanisms to select and adapt sectors
Multiple streams (MIMO) for 11ay
Edward Knightly
!"
!#
!$
%
"
%#
%$
RF
!"
!#
!$
%
"
%#
%$
RF

## Slide 14: Wi-Fi Beam Training
Sector Level Sweep
  Test transmission in each direction
  Transmit sector ID coded in transmission
  Receiver “quasi omni-directional” antenna pattern
  Receiver identifies strongest TX sector and feeds back
  Repeat in both directions

## Slide 15: Wi-Fi Beam Training
Sector Level Sweep
  Test transmission in each direction
  Transmit sector ID coded in transmission
  Receiver “quasi omni-directional” antenna pattern
  Receiver identifies strongest TX sector and feeds back
  Repeat in both directions

## Slide 16: Directional Beams and Mobility
Sector sweep yields best beam pair, until…
Mobility-induced beam misalignment
rotation
translation

## Slide 17: Directional Beams and Mobility
Blockage due to environmental mobility

## Slide 18: Directional Beams and Mobility
Blockage due to environmental mobility

## Slide 19: Timescales of Mobility Induced Outage
Blockage and misalignment can break links
  Temporary outage until re-aligned
Training overhead to recover from link breakage
  Training time can exceed data transmission time
  Each sector is a short control message with PHY/MAC headers
  Exhaustive search over all sectors at both ends

## Slide 20: Control Plane Challenge
Frequent re-training and overhead to maintain directional link can yield throughput << PHY rate
High directivity for higher data rate increases control plane overhead
Can we rapidly re-steer beams?

## Slide 21: “New” Devices Above 100 GHz
Leaky Wave Antenna (LWA)
  Metal parallel-plate waveguide
  Narrow slot open in one side
  Angular dispersion: higher input frequencies emit at lower angle
𝜙
!
𝑧
𝜙!
𝜌
b
𝜙# = sin
$%
𝑐
2𝑏𝑓

## Slide 22: Leaky Wave Antenna

## Slide 23: Couples Emission Angle & Frequency
10
20
30
40
70
80
Emission Angle (°)
0.1
0.7
0.6
0.5
0.4
0.3
0.2
0.8
0.9
Spectral Peak (THz)
f (THz)
50 60
∅! (𝑑𝑒𝑔𝑟𝑒𝑒𝑠)
fblue >fgreen
Yields highest frequency beam steering mechanism to date
One antenna beam steering (without phased array, without MIMO)
Where to steer? Where is the client?
#
𝜙 = sin$%
𝑐
2𝑏𝑓

## Slide 24: Key Idea: THz Rainbow
Idea: excite the Leaky Wave Antenna with a broadband pulse (all frequencies!)
Emits in all directions
Each direction has its own spectral signature

## Slide 25: One Shot Location Discovery
With a single nano-second scale transmission, all receivers know their relative angle
  No trial-and-error testing of directions
  No phase information needed
  No array signal processing

## Slide 26: Modeling Reception
Maxwell’s Equations predict peak emission angle
Can also characterize decay as move off peak using LWA parameters
10
20
30
60
70
80
40 50
Emission Angle (°)
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
Spectral Peak (THz)
10
20
30
60
70
80
40 50
Angle (degrees)
0.2
0.3
0.4
0.5
0.6
Frequency (THz)
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
E �  sinc kPPWG  j  k0 cos �L 2
#
𝜙 = sin$%
𝑐
2𝑏𝑓
Edward Knightly

## Slide 27: Inference Approach
Spectral signature for each angle of the rainbow
  Inspired by EM analysis
  Angle of arrival estimate is best match
  LWA imperfections and higher modes (TE2, TE3, and TE4)
Theory vs. Practice
Edward Knightly
10
20
30
60
70
80
40 50
Angle (degrees)
0.2
0.3
0.4
0.5
0.6
Frequency (THz)
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
10
20
30
60
70
80
40 50
Angle (degrees)
0.2
0.3
0.4
0.5
0.6
Frequency (THz)
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1

## Slide 28: Angle Inference Accuracy
AoA estimation error
< 5º in over 80% of cases
Spectrum only, no phase information needed
A single-shot measurement
10
20
30 40 50 60
Measured angle (degrees)
70
80
10
20
30
40
50
60
70
80
Estimated angle (degrees)
0
12
0.0
0.5
1.0
Empirical distribution function
2 4 6 8 10
Estimation error (degrees)
Y. Ghasempour et al., Nature Communications, 11(1):2017, April 2020.

## Slide 29: Radar
Radar sweeps directions, mechanically or electronically
Image source: Wikipedia

## Slide 30: New Sensing Capabilities
THz Radar with LWA: frequency embeds location information
Experiment (Mittleman Lab): move metal rod with 10 mm radius along triangle
  Accuracy of 1 mm and 1.2º
  Real time computation 200 msec
Y. Amarasinghe et al., Optics Express 28, 17997 (2020)
Object
R

leaky-wave waveguide
Edward Knightly

## Slide 31: CMOS Circuit Realization from 360-400 GHz
H.Saeidi, et al., "THz Prism: One Shot Simultaneous Localization of Multiple Wireless Nodes with Leaky-wave THz Antennas and Transceivers in CMOS," IEEE J.Solid-State Circuits , vol. 56, no. 12,
pp. 3840-3854, Dec. 2021.
𝑃𝑜𝑟𝑡 1
𝑃𝑜𝑟𝑡 2
𝑃𝑜𝑟𝑡 3
𝑃𝑜𝑟𝑡
4

## Slide 32: Sensing and Communication Take Away Message
Beam ID x
Phased array
Unique ID for each beam
Trial-and-error testing
micro-second scale
Array processing localization
New devices and physics
Single antenna
Spectral signature at each angle
All directions at once
Nano-second scale
Fast high-resolution radar

## Slide 33: Final Challenge
Final Challenge:
Blockage without Specular NLOS Path
Blockage due to environmental mobility
Suppose there is no wall

## Slide 34: Final Challenge
Final Challenge:
Blockage without Specular NLOS Path
Blockage due to environmental mobility
Suppose there is no wall
Objective: curve the beam around the obstacle

## Slide 35: Programming Wavefronts
Can we curve a beam? Does Maxwell object?
Airy beams
  Quadratic path
  Satisfy Maxwell’s Equations
  A solution to Helmholtz equation
How to generate one?

## Slide 36: Airy Beam Theory
Launch wave with initial spatial profile (amplitude and phase of radiating elements located at position x):
𝑥
Yields a quadratically curved wave
𝑥)
Φ 𝑥 = 𝐴𝑖𝑟𝑦 𝑒𝑥𝑝 𝑎 𝑥
𝑥)
1
𝐴𝑖𝑟𝑦 𝑥 = 𝜋 -
)
* 𝑡+
cos 3 + 𝑥𝑡
𝑑𝑡

## Slide 37: Airy Beam vs. Traditional Beamforming
Beamforming
Constant amplitude profile
Linear phase profile (slope controls steering direction)
Airy beam
Non linear amplitude profile
Alternating phase profile [0, 𝜋]

## Slide 38: How to Realize Airy Profile
Approach
  Discretize the Airy beam’s spatial profile Φ 𝑥
  Radiate waves from multiple points in space, each wave having the required profile
Transmit maximum
amplitude and no
Solution space
  Antenna array: lacks the spatial resolution and array size
  Metasurface: 2-D structure with sub- wavelength meta-atoms that shape wave’s profile
phase offset here
Transmit nothing here (near 0)

## Slide 39: Building Block: Meta Atom
Meta Atom: radiating element
  Sub-wavelength size metallic structure
  Acts as a very small antenna
  Split Ring Resonator
  Parameters to control amplitude, phase, and polarity
    radius 𝑟
    opening angle 𝛼
    orientation angle β
Atom-by-atom configuration
  Working together, provide the desired function Φ 𝑥

## Slide 40: Airy Metasurface Design
Select meta-atom orientation to match the function Φ 𝑥
Tile on the metasurface (in columns along x)

## Slide 41: Fabricating Metasurfaces
Hot stamped static MS
Rapid prototyping
Inexpensive
CMOS programmable MS
Programmable
Open/short ring segments
H. Guerboukha et al., Optics Express 2021.
S. Venkatesh et al., Nature Electronics 2020.

## Slide 42: Airy Metasurface Experiments
Setup
  Small-scale experiment with sub 𝜇W TDS transmitter
  Hot-stamped 150 GHz transmissive metasurface
Curved profile
Less than model
  Spatially sampled Φ 𝑥
  Imperfect meta-atoms
Edward Knightly

## Slide 43: Future Work: Airy Networks
At scale experiments including obstacles
Control plane: how to aim the curve ball
  Where is the target?
  Best curvature profile and steering angle
  Programmable metasurface
Data plane
  Sending data
Image source: The Indian Express
J. Jornet, E. Knightly, and D. Mittleman, “Wireless Communications, Sensing, and Security above 100 GHz,” Nature Communications, 2023

## Slide 44: Upcoming Wireless Advances
Network design, optimization and management to harness new antenna and metasurface capabilities
Radically transformed networks architectures fusing diverse spectrum from sub 6 GHz to THz
Programmable, low cost, energy efficient components
Sensing and learning including physical models vs. black box
New applications and use cases

## Slide 45: Summary

## Slide 46: Acknowledgements
Ph.D. students and alumni at http://networks.rice.edu
Collaborators at Rice and beyond:
  Dan Mittleman at Brown University
  Josep Jornet at Northeastern University
  Kaushik Sengupta at Princeton University
Sponsors